## Slide 1: ECE 5345
Random Processes - Stationary Random Processes

## Slide 2: Random Processes - Stationary Random Processes
Stationary Random Processes: The stochastic process does not change character with respect to time.
Examples
Types
  Strict stationarity
  Stationary in the Wide Sense (Wide Sense Stationary)
Cyclostationary - stationary in a periodic sense

## Slide 3: Strict Stationarity
X(t) is stationary in the strict sense if, for all k and  and choices of (t1, t2…, tk ),
In other words, all CDF’s are independent of the choice of time origin.

## Slide 4: Strict Stationarity-example
All iid random processes are strictly stationary. Using continuous notation…

## Slide 5: Strict Stationarity-example
The telegraph signal is strict sense stationary when the origin is randomized with a 50-50 coin flip (see the Flip Theorem) . Using independent increment property:
Substituting gives the same results!

## Slide 6: Strict Stationarity: necessary conditions
If X(t) is stationary in the strict sense,
  the mean is a constant for all time
  The autocorrelation is a function of the distance between the points only
  Note: In 2, autocovariance could be substituted with autocorrelation with the same result.

## Slide 7: Wide Sense Stationarity RP’s
X(t) is wide sense stationary if
  The mean is a constant for all time
  The autocovariance is a function of the distance between the points only
  Notes:
  In 2, autocovariance could be substituted with autocorrelation with the same result.
  All strictly stationary processes are wide sense stationary

## Slide 8: Wide Sense Stationarity RP’s: Average Power
Recall average power
In general
Thus
If X(t) is wide sense stationary, this means
If you stick your finger in a socket, this is what you feel

## Slide 9: Wide Sense Stationarity RP’s: Average Power Example
Let everything but  be fixed in the stochastic process
Then
And
Then X(t) is wide sense stationary, with
And
Recall rms voltage of a sinusoid

## Slide 10: Wide Sense Stationarity RP’s: Autocorrelation Properties
To characterize a WSS process, need (a) the mean and (b) the autocorrelation.
How to estimate empirically?

## Slide 11: Wide Sense Stationarity RP’s: Autocorrelation Properties
Proof
quod erat demonstrandum

## Slide 12: Wide Sense Stationarity RP’s: Autocorrelation Properties
3.
Proof: Recall
If X(t) is zero mean,
or
This is even true when X(t) is not zero mean. The desired result follows immediately.
quod erat demonstrandum

## Slide 13: Wide Sense Stationarity RP’s: Autocorrelation Properties
4. If for some  > 0,
then is a periodic function.
Example: Recall sinusoid
with random phase.
p.361

## Slide 14: Cyclostationary RP’s:
For a given time interval (period) T, the behavior of the process on each period has the same character.
Cyclostationary in the strict sense

## Slide 15: Cyclostationary RP’s:
Cyclostationary in the strict sense example. Let A be a random variable and define
This RP is cyclostationary in the strict sense with

## Slide 16: Wide Sense Cyclostationary RP’s: